WVU NSRR
Serial Communications Subsystem

# General Subsystem Requirements
SCSY-1	Maintain a success rate for serial communications of packets of greater than or equal 99.9% [TBR-4]
SCSY-2	Transmit and receive serial data a 115,200 bits per second using 8 data bits, 1 stop bit, and no parity

# General Software Requirements
SCSW-1	Transmit and receive the data structures defined as packet types in [TBD-1].
SCSW-2	Transmit packets at the rates defined per packet type in [TBD-1].
SCSW-3	For good packets, publish all packet body data elements received on ROS computers as ROS messages over ROS topics per data structures defined in [TBD-2] at the rate received.
SCSW-4	Obtain data to transmit in serial data packets by subscribing to the ROS topics defined in [TBD-2] .
SCSW-5	[TBR-1] Transmit last received ROS topic message values when scheduled serial transmit time arrives.
SCSW-6	Compute a checksum for the combined packet header and body [TBR-2] and append as the last byte of the packet data structure.
SCSW-7	Compute checksums using simple byte-by-byte addition ignoring overflows [TBR-3].

# Error Handling Software Requirements
SCSW-10	When a bad serial packet is received on an ROS computer, increment the packet error count, flush the associated serial buffer, and publish a bad packet ROS topic message.
SCSW-11	Declare packets as bad when they do not meet the defined packet structure for packet header characters and number of bytes.
SCSW-12	Compute the checksum of received packets and declare packets as bad for checksums that do not match.

# Appendix A: To Be Determined (TBD) and To Be Resolved (TBR) Decisions

TBD-1	Interface Definition Document for definitions of serial packet structures – currently Gu presentation file.
TBD-2	Interface Definition Document for definitions of ROS Topics.

TBR-1	Determine when data scheduled for serial transmission is considered stale and whether stale data indicators need to be transmitted with serial data.
TBR-2	Decide whether packet checksums include the header and the body or just the body.
TBR-3	Determine whether more sophisticated checksum computations are warranted.
TBR-4	Decide what data transmission success rate is required.